TB8 Outline
Dante Morelli, 12/04/25

16-bit	External Address Bus
8-bit	External Data Bus
6-bit	Transport Address Bus
8-bit	Transport Data Bus

Load instructions pull data from transport bus or immediate into buffer.
Store instructions push data from buffer onto transport bus.

bit	7	6	5..0
ld	0	0	source
ldi	0	1	immediate
st	1	0	destination
stc	1	1	destination

ld:	Load data from source location into transport buffer
ldi:	Load data from 6-bit immediate into transport buffer
st:	Store data from transport buffer into destination location
stc:	Store data from transport buffer into destination location if ALU comparator is true

Control Registers
type	7..6	5..4	3	2	1	0
ALU	Comparator Control / 00: = / 01: > / 10: < / 11: bit(s) set	Carry/M Control / 00: Forced on / 01: Forced off / 10: Looped / 11: M mode	S3	S2	S1	S0